# Creating a Standard Interface for Receiving TUIO Input from the Linux Kernel
Pavan Trikutam / California Polytechnic University / ptrikuta@calpoly.edu	Henry Phan / California Polytechnic University / htphan@calpoly.edu	Ian Stewart / California Polytechnic University / istewart@calpoly.edu

### ABSTRACT
(To be written upon project completion.)

### General Terms
TUIO, TUIODriver, TUIOMouse, tracker, client

### Keywords
Multi-touch, TUIO, Linux

### 1. INTRODUCTION
Multi-touch technology has become quite popular recently, following the 2007 introduction of iPhone by Apple and the debut of surface computing by Microsoft. The use of multi-touch technology is expected to continue to grow rapidly; for example, multi-touch phones are expected to grow from fewer than 200,000 units in 2006 to more than 21,000,000 units in 2012 [1].

Some work has been done to bring multi-touch to the GNU/Linux platform. The Tangible User Interface Object (TUIO) protocol was developed to provide a method of communication between multi-touch tracking applications and multi-touch-aware client applications [2]. TUIO provides a general and versatile communication interface between tangible table-top controller interfaces and underlying application layers. Designed to meet the needs of table-top interactive multi-touch surfaces, it is quickly becoming a standard for providing an interface for applications and touch tracking systems to communicate.

On the application side, there has a been a development in the Linux community to support multiple mice. Multi-pointer X (MPX) was developed as a set of modifications to X.Org to allow multiple independent mouse pointers to be used in the windowing system, and was merged into X.Org in 2008 [3]. MPX changes the X Server's input subsystem to allow multiple independent input devices (including keyboards, not just mice) to operate simultaneously [5]. MPX also introduced a new set of events to enable touch screens with multiple touch-points to interact with applications [5].

Currently, there is no standard source for applications to receive multi-touch input on GNU/Linux. TUIO does provide a protocol for multi-touch trackers and clients to communicate, however the developers of TUIO have left it to the community to decide how to use it. Though there exist a number of TUIO-enabled tracker applications, there is no standard common source to grab this input for client applications. As can be seen in Illustration 1, TUIO is merely a means of communication – the client and trackers vary from implementation to implementation. Developers using TUIO must provide their own trackers, and often have parallel duplicate efforts to create a source for TUIO input, which translates into wasted time and effort.

In this paper, we describe our implementation of a solution to this problem: a kernel-level device driver which userspace and kernel-level programs can poll for multi-touch input data. We call this driver TUIODriver. TUIODriver simply outputs TUIO messages when read; this approach allows developers to get TUIO data directly, or to layer an adapter over TUIODriver to convert TUIO messages into other forms of input data.

As an example of this extra layer, we provide the implementation of TUIOMouse, an adapter between TUIODriver and the Linux input module. It shows a potential use of TUIODriver as a source of TUIO input. It receives touch event information in the TUIO protocol via TUIODriver. It then simulates these touch events by creating mouse input events in X.org. A benefit of TUIOMouse is that it provides an implementation that allows developers to see legacy applications working with touch events passed through the TUIO protocol.

### 2. PROJECT OVERVIEW
TUIO is being more and more commonly used throughout the tangible user interface world, and will soon become an industry standard. TUIO provides a means of communication for interactive surfaces; however, it does not provide a location from which to access this information. In order for a true multi-touch system to remain versatile and provide extensibility, some layer of abstraction is necessary. Our project provides this layer of abstraction.

We offer a central location from which an application or window management system can grab TUIO data, implemented as a character device provided by a Linux kernel module. This central location allows development of applications within a Linux system independent on the actual source of the interaction events. Our goal is to have this central location, along with TUIO as well, become an industry standard for using the TUIO protocol in window management systems and other applications.

#### 2.1 TUIO
TUIO defines a protocol as well as an API for tangible multi-touch surfaces. The protocol provides an abstract description of a tangible surface allowing for the transmission of touch events as well as generic object states. As can be seen in illustration 1, control data is typically provided by a tracker application; the data is encoded into the protocol and is then provided to a client application.

Illustration 1: Common usage of TUIO
TUIO is based on Open Sound Control (OSC), a network-oriented communication protocol typically used for multimedia devices and sound synthesizers. Although both TUIO and OSC are most commonly implemented using network protocols such as UDP or TCP, the use of network protocols is not a requirement.

The TUIO 1.0 protocol specification defines two main message types: set and alive [2]. Set messages communicate information regarding an object's state, such as position and orientation. Alive messages indicate the current set of objects that are present on the surface. A list of unique session Ids are used to describe these objects. A third type of message, fseq messages, is included in the protocol to uniquely tag each update step with a frame sequence ID associated with the set of set and alive messages [2]. Each message is given in the following format:

/tuio/[profileName] set [sessionID parameterList]

/tuio/[profileName] alive [list of active sessionIDs]

/tuio/[profileName] fseq [int32]

TUIO messages do not have a defined packet length. Each message is associated with a profile to help define the message format and to specify any related messages (if any).

The protocol defines a few profiles to handle most situations and allows for custom profiles. Profiles allow the tracking of objects and cursors on two dimensional surfaces and, in special cases, also in the 3D space above the table surface [2]. The following are the profiles for set messages for cursors and generic objects on a 2D surface:

/tuio/2Dcur set s x y X Y m

/tuio/2Dobj set s i x y a X Y A m r

The parameters for the 2Dcur set message represent session ID, x position, y position, x velocity, y velocity, and acceleration, respectively.

In order, the parameters for the 2Dobj set message represent session ID, class ID, x position, y position, rotation angle, x velocity, y velocity, rotational velocity, acceleration, and rotational acceleration.

#### 2.2 A Central Source of Input
As can be seen in Illustration 1, TUIO is commonly used in a three-part system involving a tracker which provides control data and a client which expects control data. TUIO provides the third part of the system by providing a protocol to allow the tracker and client to communicate. While this concept works well for individual application stacks, such as digital music synthesizers, when implemented in modern desktop environments, it creates a very tight coupling between the input provider and the applications using that input.

In modern desktop environments, multiple applications may wish to obtain input from the same provider. One way for the applications to do this would be to communicate directly to the provider; however, this method creates unnecessary overhead in the form of redundant connections to the provider.
To avoid the redundant connections, a developer could create a central input “dispatcher” application that would communicate directly with the input provider and provide the client applications with input data. This would require the input dispatcher to have specific knowledge about the input provider or it would require a designated socket to communicate through. While this method would be sufficient in fully providing the desired functionality, it does not follow the tradition of Linux input devices and produces too tight of a coupling between the provider and input system.

We propose the creation of a single, central device to provide the necessary level of abstraction between the input provider and interactive applications. This follows the Linux tradition in which input devices are collected in the /dev/ filesystem‚ in most Linux systems, user input is collected through pseudofiles located in the /dev/input directory. We would make touch input data available through the device filesystem in a location such as /dev/tuio.

Our method would also allow devices to be “layered” on top of each other. For example, one could create a layered device driver that would receive TUIO touch data and use it to simulate mouse events using the Linux input module. (We provide an example implementation of this driver as TUIOMouse; Illustration 2 shows the layout.)

### 3. IMPLEMENTATION
Our implementation is comprised of two character devices, as can be seen in the simple architecture diagram in Illustration 2. It is a layered device architecture. On the bottom layer, we have TUIODriver. On the top layer, we have TUIOMouse. Our design is extensible and other applications can put it to use however they wish. The overall function of the two components in our implementation is to convert TUIO data packed in the OSC protocol into mouse events that are sent to X.Org in order to simulate mouse clicks and movements. Further description of the two components follows below.

Illustration 2: An overview of our layered devices

#### 3.1 TUIODriver
TUIODriver is our bottom-layer character device in our framework. The goal of this device is to provide a one-stop place where raw TUIO data can be retrieved. It accepts the basic character device operations: read, write, open, close, and delete. For the write operation, the device accepts raw TUIO data. When a user tries to read from TUIODriver, this stored raw TUIO data is returned. TUIODriver stores this data in a local ring buffer within the device. A ring buffer is a data structure that uses a single, fixed-size buffer as if it were connected from end to end. Ring buffers are commonly used to buffer data streams. As a result of the ring buffer implementation, the device only supports one reader and one writer at a time, which is explained in more detail later in this section.

There are a few things worth noting about this driver's implementation. Data will be constantly being written to the driver every millisecond, and storing all that information will most likely be difficult and unnecessary. When a mouse is moving, if a small portion of the mouse's path is lost, the ultimate result will still be the same: the mouse will end up in the place it's supposed to be, with only a small jump in its path. This will occur because if some of the data of the mouse's path is overwritten, it will only be overwritten with the mouse's new location, thus making the mouse's location as up-to-date as possible.

These are some things to note about our storage of data in the device's buffer. Due to scheduling, there are typically 3 sequential writes to the device (the 3 writes correspond to the 3 type of messages that the TUIO protocol supports) from the daemon we wrote to unpack TUIO from the OSC protocol. These writes happen many times a second.

We originally had a simpler implementation of the storage buffer within TUIODriver. Originally, the device simply overwrite the entire buffer every time data was written to the device. The advantage of implementing the buffer this way was that it would provide the most recent data received by the device at all times. Since the data read from the device will always be the most recent, there will be little lag when actually moving a mouse when it comes to representing its latest position. The disadvantage of this implementation of the buffer is that there was a larger amount of data lost. This is because every time data was written to the device (which happened many times a second), all the data that was written to it before that moment is overwritten. The effect of this issue was incomplete messages being stored in our device, which are of no use to anyone.

To rectify this situation, we implemented a ring buffer within TUIODriver. TUIODriver stores a number of messages within the ring buffer. Initially, data is written to the device as with the regular buffer. However, when the maximum number of messages that can be stored within the ring buffer are written to the device before any reads occur, the device begins to overwrite the old data. When the next read occurs, the oldest message is returned. It's a First In First Out buffer, meaning only the oldest data within the buffer will be overwritten at any time. This might seem a bit peculiar, since a read does not return the newest data. However, it worked very well for our implementation as a process usually usually receives multiple sequential read/writes before being rescheduled.

As mentioned earlier, using a ring buffer resulted in restricting the device to support only a single reader and a single writer at any given time. We implement this restriction because if there were multiple users reading from the device at once, the buffer would have many concurrency issues. A user might get one of the 3 required messages, get rescheduled, and in the meantime while that user is blocked another might begin a read on the device and would read the remaining two messages, resulting in both users reading an incomplete set of messages. If a process tries to open the busy device, an -EBUSY is returned.

Though allowing only one reader at a time may be undesirable, it's well worth the cost for the increased reliability and speed from the original design. The benefit of the increased speed and reliability is truly seen if we are trying to reflect the mouse's path accurately. It loses less data than a regular buffer that gets overwritten every time. For example, if someone is trying to draw a path using some kind of visual program (i.e. Photoshop), a slight delay would be a worthwhile tradeoff as long as the overall path is maintained as is.

Another advantage of having only a single user at a time is the ability to perform blocking reads. Because there is only a single reader/writer we can synchronize the pointers in the ring buffer and determine whether or not there is new data to be read. If there is none, the read function joins a wait queue and blocks until a write notifies the TUIODriver of new data arriving. A process that is reading TUIODriver will never receive an end of file; the process will just continue to block until new data arrives or the process is forced out. This behavior can be seen when performing a cat operation on /dev/TUIODriver. When performed, messages will be continually displayed until the process is manually terminated.

The main differences between the two implementations is speed and reliability of the information. One final thing to note is that either way, for the driver to serve its purpose successfully, it must be polled constantly. If it isn't polled on a frequent and consistent basis, much of the information passed to it will be lost, regardless of how we implement the buffer.

#### 3.2 TUIOMouse
TUIOMouse is responsible for collecting TUIO data from TUIODriver and using that data to simulate a traditional mouse. The mouse is simulated using the Linux input module; mouse input is simulated by simulating mouse events.

(To be completed upon further research and development.)

### 4. PERFORMANCE AND ANALYSIS

Illustration 3: touchlib's Processed Webcam Image
The hardware we used for creating a touchpad is relatively simple. The basic idea is that there will be a sheet of glass with a webcam directly under it. The webcam is what will be capturing the data and sending it to the computer. On the other side of the glass, a few millimeters above its surface, we have an array of lasers that shoot across the glass. The lasers are placed on each corner of the rectangular glass and shoot through a small lens which diffracts the laser, so that the entire sheet of glass is covered in lasers. When a finger touches the glass, it will interrupt the lasers, which is how we will be recognizing the touches. These touches will be referred to as blobs, because that's what they look like to the webcam. The webcam will transmit this data to a blob detection program, which will convert the image that the webcam sees into data sent through the TUIO protocol. An example is show in Illustration 3, which is a processed webcam image. The glowing white spots are the blobs described earlier.
Illustration 4: Entire Architecture of Our Testing Environment

As can be seen in Illustration 4, we used a number of different tools in order to test our framework. An application we found, called touchlib, runs in user space receiving and processing data from the webcam. It uses this webcam data to produce blob information that it sends through the TUIO protocol. This blob information will eventually be turned into a simulated mouse in X.Org. The blob information is written from touchlib to the socket 3333 via TUIO and OSC. We wrote a daemon running in user space called tuiod which reads from this socket and unpacks the TUIO data from the OSC protocol and formats it into strings. These strings are in turn written to TUIODriver. TUIODriver stores this data in a buffer. TUIOMouse reads this information from TUIODriver on a frequent and consistent basis.

TUIOMouse uses the information read from TUIODriver to simulate a mouse in X.Org for each of the independent touches it receives. To aid us in accomplishing this task, we use the Linux kernel module "input". This module accepts mouse event data and converts it into mouse information usable by X.Org.

### 5. RELATED WORK
Ryan Huffman has proposed the creation of an X.Org input driver which would receive TUIO input directly and convert it to MPX input [4]. We are uncertain as to how much progress he has made on his project.

### 6. FUTURE WORK
Given the “layerability” of TUIODriver, we have several future projects in mind:

The first would be an X.Org input driver, similar to the one Huffman proposed. However, our X.Org input driver would get its data from TUIODriver, and not an independent tracker.

Another project would be a second “glue” driver similar to TUIOMouse; however, this driver would accept input from TUIODriver and produce Linux input events instead.

### 7. CONCLUSION
(To be written upon project completion.)

### 8. REFERENCES
[1] http://www.usatoday.com/tech/products/2007-06-21-1895245927_x.htm

[2] http://www.tuio.org/

[3] http://wearables.unisa.edu.au/mpx/?q=mpx

[4] http://nuigroup.com/forums/viewthread/4975/

[5] http://www.linux.org.au/2008/programme/detail%3FTalkID=88.html